## Slide 1: Tree Cutting
In Shore land Zone

## Slide 2: First step is to determine where the 100’ high water setback is.
100’
High water Setback Line

## Slide 3: Then we divide your lot into 25’ x 50 rectangles
100’
150’
25’
25’
25’
25’
50’
100’
50’
Box 1
Box 2
Box 3
Box 4
Box 5
Box 6
Box 7
Box 8

## Slide 4: Count the number of trees in the rectangle
50’
25’ Box 1

## Slide 5: Each tree has a point value
Diameter of trunk measured at 4.5’ above grade
Under 3” diameter 1 Point
4”-7” diameter 2 Points
8”-11” diameter 4 Points
12” + diameter 8 Points

## Slide 6
4 points 50’
8 points 1 Point 4 Points
25’ Box 1 4 Points
4 Points
2 Points 8 Points 4 Points
Water

## Slide 7
4 points 50’
8 points 1 Point 4 Points
25’ Box 1 4 Points
4 Points
2 Points 8 Points 4 Points
Add all points together
1 points (3x1)= 3 4 points (6x4)= 24 3+2+24+16=45 points
2 points (1 x2)=2 8 points (2x8)= 16

## Slide 8: Points
There are 45 points in this rectangle. Once you are done cutting trees there needs to be at least 24 points remaining. You can cut a maximum of 21 points in this rectangle.

## Slide 9: Other things to consider:
There needs to be 24 points remaining
You can’t remove more than 250 sqft of the canopy (meaning you take a large tree out you might max out the area)
Saplings under 3’ high can’t be removed
Stumps must remain

## Slide 10: Replanting:
Replanting must be done as close as practical of existing tree
Replanting must be 2” diameter at 4-1/2’ tall.
Native species with a mix preferred.